Service for Fiat Sedici DK08 YBS

NOTE: the engine maintenance light is on because an EGR blanking plate is fitted.

From Fiat Sedici service schedule

Check tyre conditions/wear and adjust pressure if required.

Check electric system operation headlights, direction indicators, hazard lights, passenger compartment/boot light, instrument panel warning lights, etc.).

Check windscreen wiper operation, adjust nozzles if required.

Check windscreen blade position/wear.

Check front disk brake pad wear conditions and brake pad wear indicator operation.

Check rear disk brake pad or shoes conditions and wear.

Sight inspect conditions and integrity of: bodywork and underbody protection, pipes (exhaust, fuel, brakes), rubber parts (boots, sleeves, bushes, etc.), brake and fuel system hoses, axles and axle shafts.

Change brake and clutch fluid.

Top up fluids (battery, windscreen washer, etc.).

Change accessory drive belt (V-belt).

Check and adjust handbrake lever stroke, if required.

Check and adjust tappet clearance, if required.

Check exhaust emissions/smoke.

Check cleanness of bonnet and boot locks and lever cleanness and lubrication.

Change engine oil and oil filter.

Replace air cleaner cartridge.

Change engine coolant.

Change timing belt.

Change fuel filter.

Sight inspect fuel tank condition.

Change manual transaxle gear oil.

Change transmission unit oil.

Change differential oil.

Check suspension operation.

Check steering system (electric drive).

Check engine control system operation. (through diagnostic socket)

Change pollen filter.

Inspect wheel bearings.

Inspect driving axle/Propeller shaft casing.

From Sedici forum

Replace water pump.

Replace timing belt tensioners.